# More thoughts on Elephant and Castle North Junction

Bruce Lynn (Southwark Cyclists)  2 Feb 2013

Summary

- Cycle traffic flows are rising and motor vehicle flows falling

- Already on parts of the E+C junction cycles are 40% modal share at peak times

- By 2020 likely that cycles will be >50% modal share throughout the junction

- An improved 2-way layout, Teardrop 2, is proposed with just 2 junctions

- The main junction is at the south end of the present roundabout.

- It is between an extended Newington Causeway, New Kent Rd and E+C Link Rd

- This junction is very skewed, so would need delays between phases, but might still provide an efficient solution.

1.  Average traffic flows

Dept of Transport AADF (Average annual daily flow) data for counts at 3 approaches to the roundabout have been summed.  They show that over the period 2000-2011 there has been a 200% increase in cycle traffic and a 27% fall in motor vehicle traffic.  The numbers are given in the appended spreadsheet.

These trends are likely to continue as rising fuel costs and fares cause people to drive less and to look for cheaper forms of transport, of which the bike is the best option.  Maybe the GLA policy of increasing cycling will also help.  We also know that many short commutes and other journeys are not made by bike.  But that a lot of Londoners can ride bikes, and may even possess one.  So plans need to allow for a likely further doubling of cycling by 2020, along with a further 10-20% fall in motor vehicles.

2. Cycle counts

Further counts were made on Monday Jan 28th.  Cold, rainy, windy evening.  I take my hat off to the hardy cycle commuters of South London – they were heading home and taking the lousy weather in their stride.

Table 1.

| Location | Time | Direction | Count | Est N/hour |
| --- | --- | --- | --- | --- |
| Segment between Newington Causeway and New Kent Road | 5.26-5.46 | NC to NKR | 4 | 12 |
|  |  | NC to Rdbt | 121 | 363 |
|  |  | Rdbt to NKR | 33 | 99 |
|  |  | Rdbt to Rdbt | 42 | 126 |
| At exit London Road on to Roundabout (by Bakerloo Line Station) | 5.55-6.05 | LR to Rdbt | 71 | 426 |
|  |  | Rdbt to Rdbt | 10 | 60 |
|  |  | Rdbt to LR | 2 | 12 |
| Segment between New Kent Road and Elephant and Castle Link Rd | 6.18-6.28 | NKR to EC | 13 | 78 |
|  |  | NKR to Rdbt | 1 | 6 |
|  |  | Rdbt to EC | 137 | 822 |
|  |  | Rdbt to Rdbt | 0 | 0 |

The main flows by far are from London Road and Newington Causeway to the Elephant and Castle Link Rd.

3. Modal share at peak time

Cycle counts, both mine and those in the TfL report, indicate very high cycle counts on the E&C Link Rd, Newington Causeway and London Road.  They are 30-40% modal share (Table 2).

Table 2.

| Direction | Am/pm | PCUs* | Cycles | Cycle modal share |
| --- | --- | --- | --- | --- |
| Newington Causeway to Rdbt | pm | 554 | 363 | 40% |
| E&C Link to Rdbt | am | 1742 | 912 | 34% |
| Rdbt to E&C Link | pm | 1477 | 822 | 36% |
| London Rd to Rdbt | pm | 1010 | 426 | 30% |

PCU = passenger car unit = cars/light vans + 2-3*(heavy goods vehicles and buses)

Cycle counts are in January.  PCU counts are from August.  Cycle counts in general increase by 50% between January and August.  So modal share in the summer will be higher.  In addition, looking at trend over recent years (see above) we can expect cycling numbers to double over the next 10 years.  So peak time modal share is likely to be over 50% on all arms of the junction by 2020.  Road space needs to be apportioned with this in mind!

4. Teardrop solutions: Teardrop 1.

A possible layout based on just the eastern 80% of the existing roundabout was described in the previous document.  (Because this leaves the island attached to the northwest, it looks a bit like a teardrop.)  This layout I have named Teardrop 1. It consists of 3 T-junctions at the present locations of the E+C Link Rd, the New Kent Road, and Newington Causeway.  Diagram 1 shows layout.

This diagram differs from the sketch version that has been in circulation only in detail.  Changes are mainly to the crossings at the New Kent Rd junction.  Also has a more direct cycle path from E+C Link Rd to London Road, with a branch to Newington Causeway.

There are problems with this layout.  The signalised turn lane from the roundabout to St Georges Road is short.  So when significant numbers of vehicles want to make this turn (e.g. at am peak) they will tail back and block traffic going from New Kent Road to E+C Link.  Another problem is that cyclists going south in the pm rush have to wait on the roundabout at the NKR stop line.  There can be 30 cyclists waiting.  With the proposed layout it is hard to see where these cyclists safely wait without obstructing left turning cyclists.

5. Teardrop 2

Another layout is possible.  Call this Teardrop 2.  This involves creating one major cross-roads at the south end of the island.  Because of the LT Sub-Station it is a very skewed crossing.  It is shown in diagram 2.

Newington Causeway is extended across the island to be as nearly opposite the E+C Link Rd as the Sub-station allows.  The New Kent road junction moves slightly west.  London Road enters Newington causeway at a separate T-junction more or less where it does now.  Traffic is two way between New Kent Road and E+C Link Rd, and between E+C Link Rd and Newington Causeway.  As now traffic is 1-way NW on St Georges Rd and 1-way SE on London Rd, plus a bus/cycle contraflow on London Rd.

For the big junction, lights will be at stop lines on E&C Link Rd, New Kent Rd (moved a bit west) and the Newington Causeway extension on the south side of the present roundabout.  Phases as below:

| Direction | Phase 1 | Phase 2 | Phase 3 |
| --- | --- | --- | --- |
| E+C Link to Newington Causeway Extension | G | R | R |
| E+C Link to St Georges Rd | R | G | G |
| E+C Link to New Kent Rd | G | R | R |
| Newington Causeway Extn to St Georges Rd | R | G | R |
| Newington Causeway Extn to E+C Link | R | G | R |
| Newington Causeway Extn to New Kent Rd | R | G | G |
| New Kent Rd to St Georges Rd | R | R | G |
| New Kent Rd to E+C Link Rd | G | R | G |

As phase 1 is the only green for E+C to NKR, needs to be longer as this is one of main flows for motor vehicles.  During this phase stopping the left turn from E+C Link to St Georges means cyclists can cross to the cycle path to Newington Causeway and London Rd without risk from left-turning traffic (“Left hook”).

Note the route from New Kent Road to St Georges Rd does not clog the junction now as when New Kent Rd lights are green, there is a clear lane to St Georges Rd with no further stop line.

Cycle traffic going south from Newington Causeway to E+C Link will need to avoid traffic making the left turn into NKR.  A holding area on the left is proposed.  This can be taken from the land freed up by the Teardrop 2 layout.  An alternative approach would be to give cyclists a head start at the NC stop line for London Rd, allowing them to get across to lane 2 safely.

Pedestrian crossings will be needed, with light controlled crossing phases, on each road as it approaches the system. It will not be necessary to have a crossing to the island (now a peninsula) at the end of the Newington Causeway Extension.  Due to the freeing up of space on the east side of the system, there is a good route north-south on that side without using the island (for example to get between the 2 tube stations).

The t-junction between London Road and Newington Causeway is pretty straightforward.

The big potential problem with the Teardrop 2 is the distance between the stop lines in the very skewed crossroads. From E+C Link Rd to NKR or NC Extension stop lines is 50m; from NKR to NC Extension stop lines, just a few metres. There will need to be perhaps 10 seconds delay between 2 of the 3 phases to allow traffic to clear the junction. The advantage is that one set of lights is lost compared with Teardrop 1 (or a fully signalised roundabout).  My impression, having watched the traffic at peak time with the current arrangement, is that it is certainly worth modelling Teardrop 2 to see how it copes.

Appendix 1      Average Traffic Flows

| Average annual daily flows | Elephant and Castle |  | From DoT | AADF data - major roads (by direction) |  |
| --- | --- | --- | --- | --- | --- |
| CP | 46107 | E+C Link Rd (A3) |  |  |  |  |  |  |  |
|  | 46783 | New Kent Rd (A201) |  |  |  |  |  |  |  |
|  | 56099 | Newington Causeway (A3) |  |  |  |  |  |  |
| Bi directional flows |  |  |  |  |  |  |  |  |  |
| CP | Year | All motor vehicles |  | Cycles |  |  | % cycles/total traffic | motor, %2000 | Cycle, %2000 |
|  |  | S | N | Both | S | N | Both |  |  |  |
| 46107 | 2000 | 31536 | 37640 | 69176 | 518 | 686 | 1204 | 1.7% |  |  |
|  | 2004 | 24104 | 24960 | 49064 | 755 | 1139 | 1894 | 3.7% | 71% | 157% |
|  | 2010 | 25211 | 30915 | 56126 | 2223 | 3435 | 5658 | 9.2% | 81% | 470% |
|  | 2011 | 24911 | 20781 | 45692 | 2157 | 3567 | 5724 | 11.1% | 66% | 475% |
|  |  | E/N | W/S | Both | E/N | W/S | Both |  |  |  |
| 46783 | 2000 | 25360 | 20913 | 46273 | 783 | 757 | 1540 | 3.2% |  |  |
|  | 2004 | 28653 | 21485 | 50138 | 273 | 620 | 893 | 1.7% | 108% | 58% |
|  | 2010 | 21412 | 22545 | 43957 | 2322 | 1523 | 3845 | 8.0% | 95% | 250% |
|  | 2011 | 21130 | 22250 | 43380 | 2283 | 1497 | 3780 | 8.0% | 94% | 245% |
|  |  | S | N | Both | S | N | Both |  |  |  |
| 56099 | 2000 | 11971 | 15058 | 27029 | 640 | 814 | 1454 | 5.1% |  |  |
|  | 2004 | 6738 | 9595 | 16333 | 427 | 438 | 865 | 5.0% | 60% | 59% |
|  | 2010 | 7143 | 7928 | 15071 | 1279 | 1653 | 2932 | 16.3% | 56% | 202% |
|  | 2011 | 7059 | 7830 | 14889 | 1227 | 1625 | 2852 | 16.1% | 55% | 196% |
| Total | 2000 |  |  | 142478 |  |  | 4198 | 2.9% |  |  |
|  | 2004 |  |  | 115535 |  |  | 3652 | 3.1% | 81% | 87% |
|  | 2010 |  |  | 115154 |  |  | 12435 | 9.7% | 81% | 296% |
|  | 2011 |  |  | 103961 |  |  | 12356 | 10.6% | 73% | 294% |